KUBERNETES CLUSTER CREATION

Links: https://cloud.google.com/kubernetes-engine/docs/concepts/deployment

In order to create the kubernetes cluster, we have follow some of the prequesties to create a k’8s cluster.
prerequisties:
for master:
2GB RAM (min.)
2 Cores CPU(min.)
for slave:
1GB RAM(min.)
1 Core CPU (min.)

Installation steps:
At master and node (Do the same process for both master and node only network differs master and node )
The Installation process will be same for both master and slave

- Update the repository
- Turn off swap space
- Update Hostname, Hosts & Set Static IP
- Install Open SSH server and Docker
- Install kubeadm, kubectl and kubelet
After this process, on master and node , go to the master and

Initiate Kubernetes Cluster
`	install the pod network
setup the kubernetes dashboard
commands:

Update the repo,
sudo yum update or apt-get update

Turnoff the swap space,
swapoff -a
Go the fstab file in path /etc/fstab and disbale the UUID,

# UUID=26620198-186a-404b-b9a1-12d957d7c826 / xfs defaults,noatime 1 1
- check the swap memory is disabled or not with,
free -h
edit the hostname in path /etc/hostname and add the master name,
sudo /etc/hostname

edit the hosts file and add the ip of the master and nodes and hostnames and viceversa
sudo /etc/hosts, mention as below:
127.0.0.1 localhost localhost.localdomain localhost4 localhost4.localdomain4
::1 localhost6 localhost6.localdomain6
172.31.32.11 k8master
172.31.13.123 node1
172.31.5.72 node2

create the kubernetes repo in path /etc/yum.repos.d/kubernetes.repo to get the kubernetes packages from the repo and add the following lines in that file,

[kubernetes]
name=Kubernetes baseurl=https://packages.cloud.google.com/yum/repos/kubernetes-el7-x86_64 enabled=1 gpgcheck=1 repo_gpgcheck=1 gpgkey=https://packages.cloud.google.com/yum/doc/yum-key.gpg https://packages.cloud.google.com/yum/doc/rpm-package-key.gpg

Upgrade the ip tables in the file, /etc/sysctl.conf

net.bridge.bridge-nf-call-ip6tables = 1
net.bridge.bridge-nf-call-iptables = 1
check with command,
sysctl -p
Install the kubeadm, kubectl, kubelet and docker the master and even in the node machine,
yum install -y kubeadm kubelet kubectl docker
Start and enable the kubelet service and docker (docker daemon)service,
for i in docker kubelet
> do
> systemctl start $i	(or)	systemctl start kubelet docker
> systemctl enable $i	systemctl enable kubelet docker
> done

Initialize the cluster in the master,
kubeadm init –pod-network-cidr=172.30.0.0/16

    - To start using your cluster, you need to run the following as a regular user:
  mkdir -p $HOME/.kube
    sudo cp -i /etc/kubernetes/admin.conf $HOME/.kube/config
        sudo chown $(id -u):$(id -g) $HOME/.kube/config

Alternatively, if you are the root user, you can run:

  export KUBECONFIG=/etc/kubernetes/admin.conf
A Pod Network allows nodes within the cluster to communicate. There are several available Kubernetes networking options. Use the following command to install the flannel pod network add-on:

sudo kubectl apply
-f https://raw.githubusercontent.com/coreos/flannel/master/Documentation/kube-flannel.yml

Check the status of the nodes,
sudo kubectl get nodes
Once a pod network has been installed, you can confirm that it is working by checking that the CoreDNS pod is running by typing:
sudo kubectl get pods –all-namespaces

Repeat the same installation process in the nodes and while initialisation of kubenetes in the master you’ll the statement like shown below, use the link and copy and paste in node machine to join into the cluster.

kubeadm join 172.31.32.11:6443 --token 0gtf3i.2yxe1httf05nw6mv \
--discovery-token-ca-cert-hash sha256:d2bd7748326f93c078e540258a1cde35f2b464b7261654f9b03e413a78135120kubeadm join 172.31.32.11:6443 --token 0gtf3i.2yxe1httf05nw6mv –discovery-token-ca-cert-hash sha256:d2bd7748326f93c078e540258a1cde35f2b464b7261654f9b03e413a78135120